## Slide 1
EEPROM
Yogesh M Iggalore

## Slide 2
Types of ROM
ROM : Mask Programmable ROM (MROM)
EPROM : UV Erasable ROM
OTP : One Time Programmable EPROM
EEPROM : Electrically Erasable and Programmable ROM
Flash Memory

## Slide 3
What is EEPROM
Electrically Erasable Programable Read Only Memory
It’s is non-volatile memory which keep holding data even if power is losses.
The content of EEPROM may be changed during operation (similar to RAM ), but remains permanently saved even upon the power supply goes off(similar to ROM)
It can be found inside microcontroller or outside the microcontroller
ESP8266 has 4096 bytes of EEPROM

## Slide 4
Arduino EEPROM Lib
Functions | Description
EEPROM.begin(size_t size) | This function begins eeprom with mentioned byte size max byte size is 4096 Ex: EEPROM.begin(20); // starts EEPROM with size 20 bytes
EEPROM.read(int const address) | This returns byte value stored in mentioned address ex: bValue= EEPROM.read(10); // returns value stored in address 10
EEPROM.write(int const address, uint8_t value); | This functions writes value to mentioned address. Ex: EEPROM.write(10,123); // here writes value 123 to address location 10
EEPROM.commit(); | This function stores all write values to EEPROM. EX: EEPROM.commit();