## Slide 1
ESP8266 General Purpose Input Output
Yogesh M Iggalore

## Slide 2
ESP8266-12E Pins
Label | GPIO | Input | Output | Notes
D0 | GPIO16 | no interrupt | no PWM or I2C support | HIGH at boot used to wake up from deep sleep
D1 | GPIO05 | OK | OK | often used as SCL (I2C)
D2 | GPIO04 | OK | OK | often used as SDA (I2C)
D3 | GPIO00 | pulled up | OK | connected to FLASH button, boot fails if pulled LOW
D4 | GPIO02 | pulled up | OK | HIGH at boot connected to on-board LED, boot fails if pulled LOW
D5 | GPIO14 | OK | OK | SPI (SCLK)
D6 | GPIO12 | OK | OK | SPI (MISO)
D7 | GPIO13 | OK | OK | SPI (MOSI)
D8 | GPIO15 | pulled to GND | OK | SPI (CS) Boot fails if pulled HIGH
RX | GPIO03 | OK | RX pin | HIGH at boot
TX | GPIO01 | TX pin | OK | HIGH at boot debug output at boot, boot fails if pulled LOW
A0 | ADC0 | Analog input | X | Analog pin 1.8V

## Slide 3: Drive Mode: Strong and Slow Strong
Strong Drive Mode
Slow Strong Drive Mode
Normal output mode. Works like an inverter.
Rise/Fall times 12ns Max
Controlled rise/fall times. Rise/Fall times 60 ns Max.
Saves power
GND
VCC
From MCU
core
Port Pin
To MCU Input Logic
GND
VCC
Port Pin
To MCU Input Logic
From MCU Core

## Slide 4: Drive Mode: Open Drain - Drives High/Low
Open Drain-Drives high
Connect a resistor externally from pin to ground
VCC
From PSoC Core
Port Pin
To PSoC Input Logic
GND
From PSoC Core
Port Pin
To PSoC Input Logic
Open Drain-Drives Low
Connect a resistor externally from pin to Vdd

## Slide 5: Drive Mode: Hi-Z and Analog Hi-Z
Hi-Z Mode
Digital Input Mode
GND
VCC
Port Pin
To PSoC Digital Input Logic
Analog Hi-Z Mode
Analog Input Mode.
Select when port is unused since it consumes no power.
GND
VCC
Port Pin
To PSoC Analog Input Logic

## Slide 6: Drive Mode: Resistive Pull-Up and Pull-Down
Resistive Pull-Up
Effective Circuit if written with ‘1’
VCC
Port Pin
To MCU Input Logic
5.6K
Port Pin
To MCU Input Logic
5.6K
Resistive Pull-Down
Effective Circuit if written with ‘0’
NOTE: If you are using this mode as input-only, make sure to write correct value to port!
GND
VCC
Port Pin
To MCU Input Logic
5.6K
From MCU Core
GND
VCC
Port Pin
To MCU Input Logic
5.6K
From MCU Core

## Slide 7: Example: Switches and Pushbutton Inputs
5.6K
VCC
Button
SPST Button: Produces either Vcc or Floating input.
Adding a pull-down resistor fixes it.
Port Pin
To PSoC Input Logic
5.6K
VCC
Button
PSoC port in Pull-Down mode
Don’t Forget: Write ‘0’ to port